Process description
Sensor acquires data
Message (complete)
Message (complete)
TCP takes ownership
Create sensor message
Extract headerbuffer
Extract headerbuffer
get_data_size()
get_data_ptr()
Queue sensor message
tcp_send_buffer
Create buffer (headersize)
Blocking send calls
Queue determines address
Confirm. message
Insert headerinfo
get_data_size()
Move it to addressee (TCP)
Extract databuffer
Extract databuffer
get_data_ptr()
Create buffer (empty)
tcp_send_buffer
Blocking send calls
Confirm. message
Insert data obj (cvmat)
Delete message
Message (header_buffer)
TCP receives header message
Extract headerinfo
B_head = Create header buffer
buffer(vector<char>)
Message initialized
M = create message(B_head)
B_data = M→ get_data_buffer()
TCP receives data message
B_data → insert(data) = cvmat
M →insert(data_buffer)
Message M is complete

---
Version 2.0
- Issues with 1.0
  - Streaming protocol, hence sender and receiver open the connection and then keep it open, tried with open/close after each message but needs too much handling
  - For data message, the receiver takes exactly the indicated number of bytes. Then switch to receiving header, because it is not certain if sender keeps “messages” apart or aggregates them based optimization etc.
- Currently not able to reference a specific message between sender/receiver. Hence sender should create unique id for each message which is transferred in the header. The receiver can then use the reference in confirmation/retransmit messages.

---
Header Message
Length = 3 + 1 + 4 + 4 + 1 + 1 + 4 + 4 + 3 = 21 bytes
Control seg:	encode “con”
Sender : rpi, jetson
New:
message id
Sender: unique message id
Time sent: local time at sender
Origin - Sender : arduino, rpi etc
Origin – Sensor : camera n, usensor n, imu, etc
Origin - time : local time at origin
Data - length
Control seg:	encode “end”
Data Message
Length in header
Data – raw
tcp_server.h
tcp_server.cpp
Test: tcp_reader.cpp
Sender
RPI, Jetson
Linux, little endian, 32 bit
Receiver
PC cockpit
Linux, little endian, 64 bit
TCP
Header Message
Socket, listen, connect, read
Data Message
Confirmation Message
Retransmission Message

---
Sender workflow
If valid message obj
Initialize message (header data)
Send header message
Send data message
Receive response
If response is retransmission message
Retransmit header message
Retransmit data message
If response is confirmation message
Set transmission status to success
Receive header message
Extract header information
If necessary
Delete message obj
Y
Initialize Message obj
Receive Data Message
Copy into Message obj
Control segments ok?
N
Message complete?
ie. length correct?
N
Y
‘Message complete’
Queue message
Send confirmation message
Send retransmission
message
update

---
Receiver workflow
Receive header message
Extract header information
Receive header message
If valid Header message
Initialize message obj
Receive data message
If data message valid
Complete message obj
Queue message obj
Send confirmation message
If data message not valid
Send retransmission message
If not valid Header message
Send retransmission message
Control segments ok?
Y
N
Initialize Message obj
Receive Data Message
Copy into Message obj
N
Message complete?
ie. length correct?
Y
‘Message complete’
Queue message
If necessary
Delete message obj
Send confirmation message
Send retransmission
message

---
Version 1.0
- Dropped handling based on message type
- No short/long message types anymore
- All data is transferred with header/data messages
- The header and data are transferred without confirmation in between
- The confirmation happens once when the message has been completely received
.c_str();

---
Sender
RPI, Jetson
Linux, little endian, 32 bit
TCP
Receiver
PC cockpit
Linux, little endian, 64 bit
Socket, listen, connect, read
tcp_server.h
tcp_server.cpp
Test: tcp_reader.cpp
Header Message
Header Message
Length = 3 + 1 + 4 + 1 + 1 + 4 + 4 + 3 = 21 bytes
Control seg:	encode “con”
Time sent: local time at sender
Origin - Sender : arduino, rpi etc
Origin – Sensor : camera n, usensor n, imu, etc
Origin - time : local time at origin
Data - length
Data – raw
Sender : rpi, jetson
Control seg:	encode “end”
Data Message
Length in header
Data Message
Confirmation Message
Retransmission Message

---
Sender workflow
If valid message obj
Create message header
Send header message
Send data message
Receive response
If response is retransmission message
Retransmit header message
Retransmit data message
If response is confirmation message
Set transmission status to success
Receive header message
Extract header information
If necessary
Delete message obj
Y
Initialize Message obj
Receive Data Message
Copy into Message obj
Control segments ok?
N
Message complete?
ie. length correct?
N
Y
‘Message complete’
Queue message
Send confirmation message
Send retransmission
message
update

---
Receiver workflow
Receive header message
Extract header information
Receive header message
If valid Header message
Initialize message obj
Receive data message
If data message valid
Complete message obj
Queue message obj
Send confirmation message
If data message not valid
Send retransmission message
If not valid Header message
Send retransmission message
Control segments ok?
Y
N
Initialize Message obj
Receive Data Message
Copy into Message obj
N
Message complete?
ie. length correct?
Y
‘Message complete’
Queue message
If necessary
Delete message obj
Send confirmation message
Send retransmission
message

---
Version 0.1
- Prototyping
- Simple message exchange based on …

---
Create message at sender
RPI, Jetson
32 bit
Extract header
Confirm control seg
TCP
Connection at Receiver
PC cockpit
64 bit
Socket, listen, connect, read
short
long
Determine
Data pos
Data length
Determine data length
Create message
Enter header info
Reserve message buffer
(ptr, length)
Create message
Enter header info
Copy data
Read TCP buffer
Copy to message buffer
‘Message complete’
Confirm ok
Queue message
Drop message
Request retransmission
tcp_server.h
tcp_server.cpp
Test: tcp_reader.cpp
Message Header (buffer, length)
Control seg
Time sent
Data type
Origin
Origin time
Message typ
Data length
Short message type : Data
Long message type: length = 0
Control seg:	encode “con”
Message type:
short message = header contains data
Long message = data is sent in following packets
Time sent: local time at sender
Data type: camera n, usensor n, imu, etc
Origin: data source :	arduino, rpi etc
Origin time : local time at data source
Data length:	0 for short message, # of bytes for long
Message type
Message type
Message type
Received N bytes
= message length?